## Slide 1: Smart Cleaning Robot
A ROS-Based Autonomous Cleaning Robot with Indoor Mapping,
Coverage Path Planning, Voice Control, and Expandable Functionality
A COSI 119 Autonomous Robotics Final Project
Team Members: Pang Liu, Zhenxu Chen
Presentation: Pang Liu (Nov 23, 2024)

## Slide 2: IRL Demo

## Slide 3: Gazebo Simulation Demo

## Slide 4: Modules and Responsibility Distribution
Panel Module (Pang Liu)
Self-designed GUI for program entrance
Integrated all modules in this module
Use buttons or voice to control program
Mapping Module (Zhenxu Chen)
Based on Explore_Lite package
Customized for the program
Explore fast and save the map
Two Different Cleaning Modules
Voice Control Module (Pang Liu)
Based on Vosk model
Recognize voices
Real-time monitoring in the background
Cleaning Module I (Zhenxu Chen)
Based on CCPP package and move_base
Customized for the program
Cleaning Module II (Pang Liu)
Sub Module I: Route Analysis
Fully Self-designed Route Analysis program
Load saved map and analyze cleaning route
Can mark with three kind of values: obstacles, uncleaned point, and cleaned point
Sub Module II: Route Follow
Fully Self-designed Route Follow program
DO NOT NEED move_base!

## Slide 5: Main Project Files Directory Structures
/Cleaning_Robot
/maps
/src
/cleaning_bot
/control_panel
/simulation_world
/sweep
/launch
/src
panel_sim.launch
panel_real.launch
control_panel_gui.py
{controller scripts}
*support panel & control nodes
voice_vosk.py
explore.launch
world_sim.launch
/src
/pathifiles
route_map_server.py
route_plan.py
route_show.py
route_follow.py
/turtlebot3
/ccpp
/{vosk_model}
Cleaning Module II
Panel Module
Cleaning Module I
(at branch backup)
Mapping Module
Voice Control Module

## Slide 6: Panel Module
All-in-on self designed GUI Panel to control all tasks and allow voice control.
The recognized voice will show on the panel.
Hint and instructions for people who don’t understand codes.
Can start SLAM, explore and build the map.
Can save the multiple maps.
Can load the newest map and analyze route and can show the points and route on Rviz.
Can start cleaning and stop cleaning.
Can quit program by clicking quit program.
Allow robot control, don’t worry hit the wall.
Developer Friendly:
  Can optimize route algorithm easily, just modify the algorithm in source file and click Refresh Route button.
  The ROS Log Output helps developers find bugs.

## Slide 7: Mapping Module
Step 1: Click [Start SLAM] to open the SLAM gmapping and RViz.
It will run the turtlebot3_slam.launch to start SLAM, RViz, and sensor supporting.
Step 2: Click [Start Exploration] to start frontier exploration.
It essentially runs the explore.launch, which is the launch file of the explore_lite package, used to start the robot's autonomous exploration function. Its main purpose is to allow the robot to explore unknown areas through the frontier-based exploration method and generate a complete map.

## Slide 8: Mapping Module
The robot will continue exploring the map, using frontier exploration logic.
The user can see the map and click [Save Map] to save the map.
The robot will continue exploring for one hour, and automatically save the map and stop exploration, if user doesn’t stop manually.

## Slide 9: Mapping Module
The user can manually stop exploration and save the map, or wait for the robot explore for one hour, automatically stop exploration and save the map.
The map will save in two files:
PGM and YAML files are two common file formats in ROS and robot-related applications, which are used to store map data and map metadata, respectively.

## Slide 10: Voice Control Module
Continuing Recognize Voice
Publish recognized voice as messages in voice_command topic
The panel will show the messages recognized
If the message includes key word, run corresponding button
Vosk processes audio input in real-time by extracting features from the sound and using a pre-trained acoustic and language model to convert speech into text.
The recognized text is then published in voice_command topic, and continuing listened by the panel node, enabling the script to parse and act on specific voice commands.

## Slide 11: Cleaning Module I
The Cleaning Module I use CCPP package (https://wiki.ros.org/full_coverage_path_planner) to achieve the cleaning function.
The CCPP package will use saved map to plan a full coverage route and allow the robot following the route.
Video: https://drive.google.com/file/d/1F1Hh0JKD9KMvRVsC_EX5ZwptzUVWLEi8/view?usp=drive_link

## Slide 12: Cleaning Module II: Why Self Design?
Innovative requirements for core functions:
  The cleaning function is the core function of the cleaning robot, which is directly related to the actual value and user experience of the product. In order to make the product commercially competitive and innovative, the cleaning function needs to be independently developed, rather than simply relying on existing third-party packages.
Customizability and scalability:
  Although the use of ready-made packages can quickly implement functions, it will limit the flexibility in subsequent development and cannot expand functions and optimize accuracy according to specific needs. Therefore, the development team decided to design the cleaning function from scratch to better control the development process and technical implementation.

## Slide 13: Cleaning Module II: Goal
Improve technological innovation capabilities:
  The self-developed cleaning function helps accumulate core algorithms knowledge and lays a technical foundation for future product optimization and innovation. It might seem stupid now, but with the continuous development, it will become more and more reliable and efficient.
Assist education and scientific research (Further Plan)
  The successfully developed robot cleaning function can be used as part of research and laboratory equipment to promote more scientific research cooperation and application scenario exploration.
  The project will be continuing update and will be made into a tutorial for new learners to know how to make a cleaning robot step by step.
  The frontier exploration module will also be self designed after this final term is finished completely.
  It will be reorganized to an open-source project on smart cleaning robot, and welcome everyone come to do it together!

## Slide 14: Cleaning Module II: Processing Sequence
route_map_serve.py
Route_plan.py
route_show.py
route_follow.py
Sub Module I: Route Analysis
Sub Module II: Route Follow

## Slide 15: Cleaning Module II => Sub Module I Route Plan Logic (1) – (5)
Detailed introduction of route_plan.py (core script):
  (1) Get the latest map (map data of OccupancyGrid message type) through /map topic.
  (2) Convert OccupancyGrid data to a grid map represented by a NumPy array.
  (3) Perform obstacle expansion on the map (taking into account the safety distance of the robot)
  (4) Generate a three-value map: -1, 0, and 1 are used to represent obstacles, unvisited areas, and visited areas respectively
  (5) Generate path points in the map through a fixed sampling interval. Each path point includes world coordinates and grid coordinates

## Slide 16: Cleaning Module II => Sub Module I Route Plan Logic (6) – (7)
(6) Use a greedy algorithm to find valid connections between path points and check whether there are obstacles between two points
(7) After the connection is completed, use matplotlib to draw the path points and connected line segments and save them as image。
  The logic of finding valid connections here is:
  Each path point can only be connected to the path points connected to it.
  The definition of connection is up, down, left, and right
  Isolated path points are not considered in the connection

## Slide 17: Cleaning Module II => Sub Module I Route Plan Logic
Original map file
Expand the map to include obstacles (taking into account the robot’s safety distance)
Map with waypoints and directional arrows

## Slide 18: Cleaning Module II => Sub Module I Planned Route showed in RViz
You can see red point (uncleaned point)
And the path with arrow now!!

## Slide 19: Cleaning Module II => Sub Module II Route Following (Still Debugging, Not Launched Yet)
The robot will follow the points and planned route direction, following the red points one by one.
Once it reached a red point, that point will turn to green point, meaning the point that has been cleaned.

## Slide 20: Supported Modules
/simulation_world
  Provide different simulation maps for different circumstances
  Allow testing in simulations efficiency, allowing agile development
  Use world:={map} to open corresponding map
    Eg. (bash$) roslaunch control_panel panel_sim.launch world:=house
bookstore (default)
house
warehouse

## Slide 21: Supported Modules
/turtlebot3
  Provide turtlebot3 supported gmapping SLAM, used in Mapping Module
  Provide the required support for TurtleBot3 hardware and Gazebo simulation models includes LiDAR and IMU (Inertial Measurement Unit) sensors.
Turtlebot3 Built by ourselves